## Slide 1: FreeBSD Firewalls SS-E 2014
Kevin Chege
ISOC

## Slide 2: What’s a Firewall?
Computer network security device to protect devices, or restrict access to or from a network
Analyzes traffic coming in or going out (or through it) and determines a course of action based on a pre-defined rule set
Firewalls can be found anywhere:
  On your laptop OS
  On routers
  On server OS
  On network hardware appliances

## Slide 3: Types of firewalls
Packet Filters – analyze network packets and decide a course of action based on configuration
Stateful Filters – track network “conversations” and maintain a table of which connections are in an active conversations
Application layer – aka Layer 7 firewalls are able to detect if an unwanted protocol is attempting to bypass the firewall on an allowed port

## Slide 4: Keeping State vs Stateless
Stateful inspection refers to ability to track the state, or progress, of a network connection
By storing information about each connection in a state table, a firewall is able to quickly determine if a packet passing through the firewall belongs to an already established connection.
If it does, it is passed through the firewall without going through ruleset evaluation saving time and avoiding extra processing.

## Slide 5: Typical features of a Firewall
Rule Syntax
NAT control
Able to pass, redirect or drop traffic based on the rules
Logging feature – to allow audit of activities and of traffic
Stateful inspection - not all and may need to be enabled with extra config options
Ability to be either inclusive or exclusive - An exclusive firewall allows all traffic through except for the traffic matching the ruleset. Inclusive firewall does the reverse

## Slide 6: FreeBSD Firewalls
FreeBSD ships with 3 Main firewalls:
  IPFW – IP FireWall is (by default) a stateless firewall. FreeBSD sponsored firewall software application authored and maintained by FreeBSD volunteer staff members.
  IPF – IP Filter can be configured as stateful or stateless. Open source application and has been ported to FreeBSD, NetBSD, OpenBSD, SunOS™, HP/UX, and Solaris™ operating systems. IPFILTER is actively being supported and maintained, with updated versions being released regularly.
  PF – Packet Filter can be configured as stateful or stateless. Maintained by OpenBSD Project

## Slide 7: PF (Packet Filter)
Was initially developed for OpenBSD
Has been successfully ported to many other operating systems including all the other BSDs and Mac OS X
Written by Daniel Hartmeier
Derived its rule syntax from IPFilter
Has many features

## Slide 8: Features
Can do both stateless or state-full firewalling
Can do Network Address Translation
  Additionally can do Bidirectional NAT aka One to One NAT
Combined with ALTQ (ALTernate Queueing framework for BSD) can perform QoS
  Priority queuing – assign certain traffic a higher priority than others before forwarding
  Class Based Queuing – assigning bandwidth to certain queues and reducing bandwidth for others
Can be configured for automatic fail-over between 2 boxes using CARP – Common Address Redundancy Protocol

## Slide 9: Features cont’d
FTP-proxy integration to handle FTP firewalling
Configurable logging per rule to pflogd
  Logs can be further monitored with tcpdump
Simple IP Filter rule syntax
  Eg: pass in quick on em0 inet proto tcp all
Macro definition – to simplify rule creation
  Eg identify an interface as “LAN” instead of “em0”
Support for transparent proxying with SQUID
  Redirect all traffic destined for a port 80 to the Squid port 8080 for Squid to process
Among many others

## Slide 10: Working with PF
Installed by default on FreeBSD since FreeBSD 5.3 but is disabled
Can start in from boot by adding the following to /etc/rc.conf: pf_enable=YES
  Or by kldload pf.ko
Start it by doing
  /etc/rc.d/pf start OR pfctl –e
You may want to compile pf support into the kernel to enable:
  Pfsync seudo device
  CARP for automatic failover
  ALTQ – for prioritization, bandwidth throttling

## Slide 11: Options in rc.conf
pf_enable="YES" # Enable PF (load module if required)
pf_rules="/etc/pf.conf" # rules definition file for pf
pf_flags="" # additional flags for pfctl startup
pflog_enable="YES" # start pflogd(8)
pflog_logfile="/var/log/pflog" # where pflogd should store the logfile
pflog_flags="" # additional flags for pflogd startup
You will also want to enable packet forwarding between interfaces and this can be done by
  gateway_enable=“YES” in /etc/rc.conf

## Slide 12: Working with PF
pfctl –e Enable PF
pfctl -d Disable PF
pfctl -F all -f /etc/pf.conf Flush all rules (nat, filter, state, table, etc.) and reload
pfctl -s [ rules | nat | state ] Report on the filter rules, nat rules, or state table
pfctl -vnf /etc/pf.conf Check /etc/pf.conf for errors, but do not load ruleset

## Slide 13: Packet Filtering with PF
Rules are loaded from a file usually /etc/pf.conf
Packets can be passed, redirected or dropped as they pass through an interface
PF inspects packets based on Layer 3 (IPv4/IPV6) and Layer 4 headers (TCP, UDP, ICMP/v6)
Can check for source/destination address, protocol (Layer 4) and source/destination port
Rules evaluated in sequential order – top to bottom of the file

## Slide 14: Packet Filtering with PF cont’d
A packet is evaluated against all the rules UNLESS the key word quick is specified
If quick is not specified then the last rule to match wins and action is taken on the packet
There is an implicit pass all at the beginning meaning that if a packet does not match any rule then it will be passed
You are free to circumvent this feature if you want by having a “block all” at the top of the file

## Slide 15: Rule Syntax
action [direction] [log] [quick] [on interface] [af] [proto protocol] [from src_addr [port src_port]] [to dst_addr [port dst_port]] [flags tcp_flags] [state]
action – pass or block
direction – in or out
log – should this be logged or not
quick – specified action is taken immediately
on interface – name of the interface
inet – address family, inet6 for ipv6
protocol – tcp, udp, icmp, icmp6 or others in /etc/protocols
src_addr/dst_addr – source port or destination address
src_port/dst_port – Number between 1 – 65535 (/etc/services
tcp_flags – eg flags S/SA look only for SYN and ACK
state – whether to check state. PF checks state by default

## Slide 16: Good practice
Recommended to have default deny at the beginning of the file so that what you do not specify is denied by default.
  i.e. to make it an exclusive firewall
This is to counter the default pass rule
Done by
  block in all
  block out all
Also good idea to leave out the loopback interface
  set skip on lo0

## Slide 17: Keeping state in PF
Keeping state has many advantages including simpler rulesets and better packet filtering performance.
PF is able to match packets moving in either direction to state table entries meaning that filter rules which pass returning traffic don't need to be written.
Since packets matching stateful connections don't go through ruleset evaluation, the time PF spends processing those packets can be greatly lessened.

## Slide 18: Keeping state cont’d
When a rule creates state, the first packet matching the rule creates a "state" between the sender and receiver.
Not only do packets going from the sender to receiver match the state entry and bypass ruleset evaluation, but so do the reply packets from receiver to sender.
All pass rules automatically create a state entry when a packet matches the rule. This can be explicitly disabled by using the no state option.

## Slide 19: Passing Traffic
pass in on dc0 from 192.168.0.0/24 to 192.168.0.1
pass out on dc0 from 192.168.0.1 to 192.168.0.0/24
pass in quick on em0 from 172.16.1.1 to any
pass out on em0 from any to 172.16.1.1
pass in quick on em0 inet proto icmp from any to any
pass in quick on rl0 inet proto udp from any port 53 to 192.168.0.1
What will the above rules do?

## Slide 20: Sample File
block in all
block out all
set skip on lo0
pass in on em0 inet proto tcp all
pass out on em0 inet proto tcp all
Will UDP traffic pass? Why?
Will ICMP Traffic pass? Why?

## Slide 21: Sample Rules 2
block in all
block out all
set skip on lo0
block in quick on em0 inet proto tcp from 192.168.0.1 80 to any
pass in on em0 inet proto tcp all
What happens here?

## Slide 22: Macros
Use macros to make rules simpler. Macros are usually identified at the top of the file ruleset. Sample Macros:
  ext_if=“em0”
  int_if=“em1”
  LAN=“192.168.0.0/24”
  good_ports=“{ 80, 22, 110}”
  bad_ips=“{ 172.16.0.0/23, 10.10.0.0/16,}”
  my_pc=“172.16.1.1”
Macros cannot contain a hyphen however
  so ext-if=“em0” will not work

## Slide 23: Macros cont’d
Macros are then called using the $ sign in the ruleset:
block in all
block out all
set skip on lo0
pass in on $int_if inet proto tcp from any\ $good_ports to any
block in quick on $ext_if from any $bad_ips\

## Slide 24: Other PF Features
Antispoofing - when a malicious user fakes the source IP address in packets they transmit in order to either hide their real address or to impersonate another node on the network
Anti-SPAM

## Slide 25: References and more reading
http://en.wikipedia.org/wiki/PF_%28firewall%29
http://www.openbsd.org/faq/pf/filter.html
http://www.freebsd.org/doc/en_US.ISO8859-1/books/handbook/firewalls-pf.html
http://en.wikipedia.org/wiki/Firewall_%28computing%29