## Slide 1
Domain Name System (DNS)
Joe Abley
AfNOG Workshop, AIS 2016, Gaborone
  Session-1: Fundamentals

## Slide 2: Computers use IP addresses. Why do we need names?
Names are easier for people to remember
Computers may be moved between networks, in which case their IP addresses will change.
Services might move between computers, in which case their IP addresses will change.

## Slide 3: The old solution: HOSTS.TXT
A centrally-maintained file, distributed to all hosts on the Internet
  SPARKY 128.4.13.9
  UCB-MAILGATE 4.98.133.7
  FTPHOST 200.10.194.33
  ... etc
This feature still exists:
    /etc/hosts (UNIX)
    c:\windows\hosts
Notes: Really Basic Lists (the quick & dirty way)
Addressbook
  This is where most mailing lists start - a single user enters a list of addresses into their favorite mail client in order to send messages to a group of friends without typing all the addresses each time they want to send a message:
nus Us - NANOG (hak@darkwing.uoregon.edu, hugi@oregon.uoregon.edu, jad@ns.uoregon.edu, joelja@darkwing.uoregon.edu)
Advantages
quick to implement
requires no interaction with any outside agent (listmaster, MLM software, etc.)
Disadvantages
It can quickly become a pain to keep updated
If the full list is displayed in headers, users replying to a message may end up talking to many more people than they intended to.
Individual members have no control over their participation, so they must depend on the address book owner to remove them or update their address if it changes.
Does not scale well.

## Slide 4: hosts.txt does not scale
Huge file (traffic and load)
Name collisions (name uniqueness)
Consistency
Always out of date
Single point of Administration
Did not scale well

## Slide 5: The Domain Name System was born
DNS is a distributed database for holding name to IP address (and other) information
Distributed:
  Shares the Administration
  Shares the Load
Robustness and improved performance achieved through
  replication
  and caching
Employs a client-server architecture
A critical piece of the Internet's infrastructure

## Slide 6: DNS is Hierarchical
.(root)
ma
org
com
DNS Database
/ (root)
etc
usr
bin
Unix Filesystem
Forms a tree structure
ac.ma
emi.ac.ma
afnog.org
nsrc.org
yahoo.com
ws.afnog.org
usr/local
usr/sbin
/etc/rc.d
usr/local/src

## Slide 7: DNS is Hierarchical (contd.)
Globally unique names
Administered in zones (parts of the tree)
You can give away ("delegate") control of part of the tree underneath you
Example:
  org on one set of nameservers
  afnog.org on a different set
  ws.afnog.org on a different set

## Slide 8: Domain Names are (almost) unlimited
Max 255 characters total length
Max 63 characters in each label
  RFC 1034, RFC 1035
If a domain name is being used as a host name, you should abide by some restrictions
  RFC 952 (old!)
  a-z 0-9 and minus (-) only
  No underscores ( _ )

## Slide 9: Using the DNS
A Domain Name (like www.ws.afnog.org) is the KEY to look up information
The result is one or more RESOURCE RECORDS (RRs)
There are different RRs for different types of information
You can ask for the specific type you want, or ask for "any" RRs associated with the domain name

## Slide 10: Commonly seen Resource Records (RRs)
A (address): map hostname to IPv4 address
AAAA (quad A): map a hostname to IPv6 address
PTR (pointer): map IP address to hostname
MX (mail exchanger): where to deliver mail for user@domain
CNAME (canonical name): map alternative hostname to real hostname
TXT (text): any descriptive text
NS (name server), SOA (start of authority): used for delegation and management of the DNS itself

## Slide 11: A Simple Example
Query: www.afnog.org.
Query type: A
Result:
www.afnog.org. 14400 IN A 196.216.2.4
In this case a single RR is found, but in general, multiple RRs may be returned.
  (IN is the "class" for INTERNET use of the DNS)

## Slide 12: Possible results from a Query
POSITIVE (“NOERROR”)
  the name exists, and has zero or more RRs associated with it
NEGATIVE (“NXDOMAIN”)
  the name does not exist
SERVER FAILURE (“SERVFAIL”)
  server is having bad hair day
FORMAT ERROR (“FORMERR”)
  the query you sent was broken in some way
REFUSED (“REFUSED”)
  not allowed to query the server

## Slide 13: How do you use an IP address as the key for a DNS query
Convert the IP address to dotted-quad
Reverse the four parts
Add ".in-addr.arpa." to the end; special domain reserved for this purpose
e.g. to find name for 193.194.185.25
Domain name: 25.185.194.193.in-addr.arpa.
Query Type: PTR
Result: ashanti.gh.com.
Known as a "reverse DNS lookup" (because we are looking up the name for an IP address, rather than the IP address for a name)

## Slide 14
?
Any Questions?

## Slide 15: DNS is a Client-Server application
(Of course - it runs across a network)
Requests and responses are most frequently carried in UDP packets, port 53
DNS can also use TCP transport, port 53
  for very large responses e.g. zone transfers
  because you want to exchange more than one query/response on a single session
  because a response you received told you to with TC=1
  because UDP is being aggressively rate-limited or blocked (e.g. to mitigate a reflection attack)

## Slide 16: There are three roles involved in DNS
Stub
Resolver
Caching
Resolver
Authoritative
Nameserver
Application
e.g. web
browser

## Slide 17: Three roles in DNS
STUB RESOLVER
  Takes request from application, formats it into UDP packet, sends to recursive resolver
RECURSIVE RESOLVER
  Returns the answer if already known
  Otherwise searches for an authoritative server which has the information
  Caches the result for future queries
AUTHORITATIVE NAMESERVER
  Contains the actual information published in the DNS by the domain owner

## Slide 18: Three roles in DNS
The SAME protocol is used for stub<-> resolver and resolver <-> auth nameserver
It is possible to configure a single name server as both a resolver and an authoritative server
But it still performs only one role for each incoming query
Common but NOT RECOMMENDED to configure in this way (we will see why later).

## Slide 19: ROLE 1: THE STUB RESOLVER
A piece of software which formats a DNS request into a DNS message, sends it to a resolver, and decodes the response when it arrives
Usually a shared library (e.g. libresolv.so under Unix) because so many applications need it
EVERY host needs a stub resolver - e.g. every Windows workstation has one

## Slide 20: How does the stub resolver find a recursive nameserver?
It has to be explicitly configured (statically, or via DHCP etc)
Must be configured with the IP ADDRESS of a cache (why not name?)
Good idea to configure more than one cache, in case the first one fails

## Slide 21: How do you choose which recursive resolver(s) to configure?
Must have PERMISSION to use it
  e.g. cache at your ISP, or your own, or a reliably public one
Prefer a nearby cache
  Minimises round-trip time and packet loss
  Can reduce traffic on your external link, since often the cache can answer without contacting other servers
Prefer a reliable cache
  Perhaps your own?

## Slide 22: Stub resolvers can be configured with default domain(s)
If "foo.bar" fails, then retry query as "foo.bar.mydomain.com"
Can save typing but adds confusion
May generate extra unnecessary traffic
Usually best avoided

## Slide 23: Example: Unix stub resolver configuration
/etc/resolv.conf
search sse.ws.afnog.org
nameserver 196.200.219.200
nameserver 196.200.223.1
That's all you need to configure a resolver

## Slide 24: Testing DNS
Just put "www.yahoo.com" in a web browser?
Why is this not a good test?

## Slide 25: Testing DNS with "dig"
"dig" is a program which just makes DNS queries and displays the results
Better than "nslookup", "host" because it shows the raw information in full
dig ws.afnog.org.
-- defaults to query type "A"
dig afnog.org. mx
-- specified query type
dig @196.200.223.1 afnog.org. mx
-- send to particular cache (overrides
/etc/resolv.conf)

## Slide 26: The trailing dot
# dig ws.afnog.org.
Prevents any default domain being appended
Get into the habit of using it always when testing DNS
  only on domain names, not IP addresses or e-mail addresses

## Slide 27
[field@term /usr/home/field]$ dig @zoe.dns.gh. downloads.dns.gh. a
; <<>> DiG 9.3.1 <<>> @zoe.dns.gh. downloads.dns.gh. a
; (1 server found)
;; global options: printcmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 34963
;; flags: qr aa rd ra; QUERY: 1, ANSWER: 2, AUTHORITY: 3, ADDITIONAL: 0
;; QUESTION SECTION:
;downloads.dns.gh. IN A
;; ANSWER SECTION:
downloads.dns.gh. 3600 IN CNAME zoe.dns.gh.
zoe.dns.gh. 3600 IN A 147.28.0.23
;; AUTHORITY SECTION:
dns.gh. 3600 IN NS zoe.dns.gh.
dns.gh. 3600 IN NS mantse.gh.com.
dns.gh. 3600 IN NS snshq902.ghanatel.com.gh.
;; Query time: 275 msec
;; SERVER: 147.28.0.23#53(147.28.0.23)
;; WHEN: Sat May 24 00:17:53 2008
;; MSG SIZE rcvd: 145

## Slide 28: Understanding output from dig
STATUS
  NOERROR: 0 or more RRs returned
  NXDOMAIN: non-existent domain
  SERVFAIL: cache could not locate answer
  REFUSED: query not available on cache server
FLAGS
  AA: Authoritative answer (not from cache)
  You can ignore the others
    QR: Query/Response (1 = Response)
    RD: Recursion Desired
    RA: Recursion Available
ANSWER: number of RRs in answer

## Slide 29: Understanding output from dig
Answer section (RRs requested)
  Each record has a Time To Live (TTL)
  Says how long the cache will keep it
Authority section
  Which nameservers are authoritative for this domain
Additional section
  More RRs (typically IP addresses for the authoritative nameservers)
Total query time
Check which server gave the response!
  If you make a typing error, the query may go to a default server