## Slide 1: Network Time Protocol (NTP)
Quick and Dirty
for AfNOG 2018
(Michuki Mwangi)‏
Original slides by Ayitey Bulley
Notes: 1

## Slide 2
About NTP
Network Time Protocol project
http://ntp.org
NTP is a protocol designed to synchronize the clocks of computers over a network.
Notes: 2

## Slide 3
About NTP
NTP version 4, a significant revision of the previous NTP standard, is the current development version. It is formalized by RFCs released by the IETF.
  RFC 5905: Network Time Protocol Version 4: Protocol and Algorithms Specification
  RFC 5906: Network Time Protocol Version 4: Autokey Specification
  RFC 5907: Definitions of Managed Objects for Network Time Protocol Version 4 (NTPv4)
  RFC 5908: Network Time Protocol (NTP) Server Option for DHCPv6
Notes: 3

## Slide 4
NTP and Time Synchronization
Network Time Protocol (NTP) is used by organizations to synchronize the clocks of all its systems.
Time synchronization is important for many reasons:
  Application time stamps
  Time stamps for log entries and audit trails.
NTP provides an easy way to ensure that all systems will maintain the same time. This can significantly simplify the burden on system administrators and tech support.
When an organization’s systems all maintain different clock times, it becomes very difficult from a troubleshooting standpoint to determine when and under what conditions a particular event might be occurring.

## Slide 5
How NTP Works
NTP works on the premise of synchronization with reference clocks, also known as ‘stratum 0‘ servers.
All other NTP servers then become a lower level strata server based upon how far they are from a reference server.
The start of the NTP chain is a stratum 1 server which is always directly connected to a stratum 0 reference clock.
From here, lower level strata servers are connected via a network connection to a higher strata level server.

## Slide 6
How NTP Works
Stratum 0
Stratum 1
Stratum 2
Stratum 3
GPS/CDMA

## Slide 7
Internal NTP Architecture
NTP 1
NTP 2
NTP 3
Internet
Strata 0/1 Servers
Stratum 2 Servers
Hosts and devices on Internal network

## Slide 8: Stratum 0 time Sources
Stratum 1 NTP servers use Stratum 0 time sources
Stratum 0 are high precision timekeeping devices also known as reference clocks
The Stratum 0 time transmission sources include;
  Atomic clocks
  Radio clocks
  Global Positioning System (GPS)

## Slide 9: Building a Stratum 1 NTP Service
Commercial approach
  Costs lots of $$$
  Plug N Play box on the network
DIY + Open Source approach
  Costs less in $ and more of time 
  Fun building execise + experience
  There are a number of Howto’s using RaspberryPi (GIY)
  SdNOG 3 presentation on building a cheap stratum 1 ntp service - https://drive.google.com/file/d/12JXTXS6is06fXZyCEiGRc-tuko6RBfrf/view

## Slide 10
Step 1: Installation of NTP Server
The first step to setting up an internal NTP structure is to install the NTP server software.
Check if the software is installed.
Update your system clock
$ sudo apt-get install ntp ntpdate
$ sudo dpkg --get-selections ntp
$ sudo dpkg -s ntp
$ sudo ntpdate –u 0.pool.ntp.org

## Slide 11
Step 2: NTP Server Configuration
Once NTP is installed, we can now configure our NTP server to synchronize with higher stratum servers.
The configuration file for NTP is stored at ‘/etc/ntp.conf’ and can be modified with any text editor.
To start the configuration process, the higher level servers need to be configured. You can use the:
  Debian default NTP pool servers in the configuration file.
  ntp.org pool servers
  List of NTP servers from NIST to specify certain servers.
  NIST’s servers in a round robin fashion (suggested method by NIST).

## Slide 12
Step 2: NTP Server Configuration
Debian default NTP pool servers in the configuration file.
ntp.org pool servers
List of NTP servers from NIST to pick specific servers.
    http://tf.nist.gov/tf-cgi/servers.cgi
server 0.debian.pool.ntp.org iburst
server 1.debian.pool.ntp.org iburst
server 2.debian.pool.ntp.org iburst
server 3.debian.pool.ntp.org iburst
server 0.pool.ntp.org iburst
server 1.pool.ntp.org iburst
server 2.pool.ntp.org iburst
server 3.pool.ntp.org iburst

## Slide 13
Step 3: Configure NTP Restrictions
NTP restrictions are used to allow or dis-allow hosts to interact with the NTP server.
The default for NTP is serve time to anyone but do not allow configuration on both IPv4 and IPv6 connections.
# By default, exchange time with everybody, but don't
# allow configuration.
restrict -4 default kod notrap nomodify nopeer noquery
restrict -6 default kod notrap nomodify nopeer noquer

## Slide 14
Step 3: Configure NTP Restrictions
Now restrict who is allowed to query the server for time and what else they are allowed to do with the NTP server.
We can also restrict the server from answering ntp queries
restrict 196.200.219.0 mask 255.255.255.0 limited kod notrap nomodify nopeer noquery
restrict 2001:43f8:0220:219:: mask ffff:ffff:ffff:ffff:: limited kod notrap nomodify nopeer noquery
# By default don’t answer anything
restrict default ignore
restrict -6 default ignore

## Slide 15
Step 3: Configure NTP Restrictions
Configure the server to unrestricted access to local users
We can also restrict the server from answering ntp queries
restrict 196.200.219.0 mask 255.255.255.0 limited kod notrap nomodify nopeer noquery
restrict 2001:43f8:0220:219:: mask ffff:ffff:ffff:ffff:: limited kod notrap nomodify nopeer noquery
# By default don’t answer anything
restrict default ignore
restrict -6 default ignore

## Slide 16
Step 3: Configure NTP Restrictions
limited: Indicates that if a client should abuse the number of packets rate control, the packets will be discarded by the sever. If the Kiss of Death packet is enabled, it will be sent back to the abusive host. The rates are configurable by an admin but the defaults are assumed here.
kod: Kiss of Death. If a host violates the limit of packets to the server, the server will respond with KoD packet to the violating host.
notrap: Decline mode 6 control messages. These control messages are used for remote logging programs.
nomodify: Prevents ntpq and ntpdc queries that would modify the server’s configuration but informational queries are still permitted.
noquery: This option prevents hosts from querying the server for information. For example without this option hosts can use ntpdc or ntpq to determine where a particular time server is getting it’s time from or other peer time servers that it may be communicating with.

## Slide 17
Step 4: Starting NTP
Startup scripts are located at /etc/init.d/
Take a look in startup script /etc/init.d/ntp
Add ntp to startup i.e. ntp to start up on boot
To Run ntp
To Restart ntp
$ sudo update-rc.d ntp enable
$ sudo service ntp start
$ sudo service ntp restart
Notes: 17

## Slide 18
Step 5: Start NTP!
$ sudo /etc/init.d/ntp start
Or
$ sudo service ntp start
Check that your server is synchronized with the ntp servers listed in /etc/ntp.conf
$ sudo ntpq -pn
$ sudo ntpq -p
remote refid st t when poll reach delay offset jitter
==============================================================================
*riditt.de 131.188.3.221 2 u 27 64 1 183.792 0.439 0.079
lofn.fancube.co .INIT. 16 u - 64 0 0.000 0.000 0.000
service1-eth3.d 228.143.95.23 2 u 28 64 1 200.457 -1.965 0.035
makaki.miuku.ne 218.186.3.36 2 u 28 64 1 377.207 -7.893 0.169
noc.mtg.afnog.o 45.222.43.250 3 u 27 64 1 0.284 1.810 0.040
Notes: 18

## Slide 19
NTP Exercises