## Slide 1
Domain Name System (DNS)
Joe Abley
AfNOG Workshop, AIS 2015, Tunis
  Session 3: Authoritative
  Name Server using BIND9

## Slide 2: Recap
DNS is a distributed database
Stub asks Resolver for information
Resolver traverses the DNS delegation tree to find Authoritative nameserver which has the information requested
Bad configuration of authoritative servers can result in broken domains

## Slide 3: DNS Replication
For every domain, we need more than one authoritative nameserver with the same information (RFC 2182)
Data is entered in one server (Master) and replicated to the others (Slave(s))
Outside world cannot tell the difference between master and slave
  NS records are returned in random order for equal load sharing
Used to be called "primary" and "secondary"

## Slide 4: Slaves connect to Master to retrieve copy of zone data
The master does not "push" data to the slaves
Master
Slave
Slave

## Slide 5: When does replication take place?
Slaves poll the master periodically - called the "Refresh Interval" - to check for new data
  Originally this was the only mechanism
With new software, master can also notify the slaves when the data changes
  Results in quicker updates
The notification is unreliable (e.g. network might lose a packet) so we still need checks at the Refresh Interval

## Slide 6: Serial Numbers
Every zone file has a Serial Number
Slave will only copy data when this number INCREASES
  Periodic UDP query to check Serial Number
  If increased, TCP transfer of zone data
It is your responsibility to increase the serial number after every change, otherwise slaves and master will be inconsistent

## Slide 7: Recommended serial number format: YYYYMMDDNN
YYYY = year
MM = month (01-12)
DD = day (01-31)
NN = number of changes today (00-99)
  e.g. if you change the file on 23rd April 2007, the serial number will be 2008052700. If you change it again on the same day, it will be 2008052701.

## Slide 8: Serial Numbers: Danger 1
If you ever decrease the serial number, the slaves will never update again until the serial number goes above its previous value
RFC1912 section 3.1 explains a method to fix this problem
At worst, you can contact all your slaves and get them to delete their copy of the zone data

## Slide 9: Serial Numbers: Danger 2
Serial no. is a 32-bit unsigned number
Range: 0 to 4,294,967,295
Any value larger than this is silently truncated
e.g. 20080527000 (note extra digit)
  = 4ACE48698 (hex)
  = ACE48698 (32 bits)
  = 2900657816
If you make this mistake, then later correct it, the serial number will have decreased

## Slide 10: Configuration of Master
/etc/namedb/named.conf points to zone file (manually created) containing your RRs
Choose a logical place to keep them
  e.g. /usr/local/etc/namedb/master/tiscali.co.uk
  or /usr/local/etc/namedb/master/uk.co.tiscali
zone "example.com" {
type master;
file "master/example.com";
allow-transfer { 192.188.58.126;
192.188.58.2; };
};

## Slide 11: Configuration of Slave
named.conf points to IP address of master and location where zone file should be created
Zone files are transferred automatically
Don't touch them!
zone "example.com" {
type slave;
masters { 192.188.58.126; };
file "slave/example.com";
allow-transfer { none; };
};

## Slide 12: Master and Slave
It's perfectly OK for one server to be Master for some zones and Slave for others
That's why we recommend keeping the files in different directories
  /usr/local/etc/namedb/master/
  /usr/local/etc/namedb/slave/
    (also, the slave directory can have appropriate permissions so that the daemon can create files)

## Slide 13: allow-transfer { ... }
Remote machines can request a transfer of the entire zone contents
By default, this is permitted to anyone
Better to restrict this
You can set a global default, and override this for each zone if required
options {
allow-transfer { 127.0.0.1; };
};

## Slide 14: Structure of a zone file
Global options
  $TTL 1d
  Sets the default TTL for all other records
SOA RR
  "Start Of Authority"
  Housekeeping information for the zone
NS RRs
  List all the nameservers for the zone, master and slaves
Other RRs
  The actual data you wish to publish

## Slide 15: Format of a Resource Record
One per line (except SOA can extend over several lines)
If you omit the Domain Name, it is the same as the previous line
TTL shortcuts: e.g. 60s, 30m, 4h, 1w2d
If you omit the TTL, uses the $TTL default value
If you omit the Class, it defaults to IN
Type and Data cannot be omitted
Comments start with SEMICOLON (;)
www 3600 IN A 212.74.112.80
Domain TTL Class Type Data

## Slide 16: Shortcuts
If the Domain Name does not end in a dot, the zone's own domain ("origin") is appended
A Domain Name of "@" means the origin itself
e.g. in zone file for example.com:
  @ means example.com.
  www means www.example.com.

## Slide 17: If you write this...
... it becomes this
$TTL 1d
@ SOA ( ... )
NS ns0
NS ns0.as9105.net.
; Main webserver
www A 212.74.112.80
MX 10 mail
example.com. 86400 IN SOA ( ... )
example.com. 86400 IN NS ns0.example.com.
example.com. 86400 IN NS ns0.as9105.net.
www.example.com. 86400 IN A 212.74.112.80
www.example.com. 86400 IN MX 10 mail.example.com.

## Slide 18: Format of the SOA record
$TTL 1d
@ 1h IN SOA ns1.example.net. joe.pooh.org. (
2004030300 ; Serial
8h ; Refresh
1h ; Retry
4w ; Expire
1h ) ; Negative
IN NS ns1.example.net.
IN NS ns2.example.net.
IN NS ns1.othernetwork.com.

## Slide 19: Format of the SOA record
ns1.example.net.
  hostname of master nameserver
jabley.hopcount.ca.
  E-mail address of responsible person, with "@" changed to dot, and trailing dot
Serial number
Refresh interval
  How often Slave checks serial number on Master
Retry interval
  How often Slave checks serial number if the Master did not respond

## Slide 20: Format of the SOA record (cont)
Expiry time
  If the slave is unable to contact the master for this period of time, it will delete its copy of the zone data
Negative / Minimum
  Old software used this as a minimum value of the TTL
  Now it is used for negative caching: indicates how long a cache may store the non-existence of a RR
RIPE-203 has recommended values
  http://www.ripe.net/ripe/docs/dns-soa.html

## Slide 21: Format of NS records
List all authoritative nameservers for the zone - master and slave(s)
Must point to HOSTNAME not IP address
$TTL 1d
@ 1h IN SOA ns1.example.net. joe.pooh.org. (
2004030300 ; Serial
8h ; Refresh
1h ; Retry
4w ; Expire
1h ) ; Negative
IN NS ns1.example.net.
IN NS ns2.example.net.
IN NS ns1.othernetwork.com.

## Slide 22: Format of other RRs
IN A 1.2.3.4
IN MX 10 mailhost.example.com.
  The number is a "preference value". Mail is delivered to the lowest-number MX first
  Must point to HOSTNAME not IP address
IN CNAME host.example.com.
IN PTR host.example.com.
IN TXT "any text you like"

## Slide 23: When you have added or changed a zone file:
Remember to increase the serial number!
named-checkzone example.com \ /usr/local/etc/namedb/master/example.com
  bind 9 feature
  reports zone file syntax errors; correct them!
named-checkconf
  reports errors in named.conf
rndc reload
  or: rndc reload example.com
tail /var/log/messages

## Slide 24: These checks are ESSENTIAL
If you have an error in named.conf or a zone file, named may continue to run but will not be authoritative for the bad zone(s)
You will be lame for the zone without realising it
Slaves will not be able to contact the master
Eventually (e.g. 4 weeks later) the slaves will expire the zone
Your domain will stop working

## Slide 25: Other checks you can do
dig +norec @x.x.x.x example.com. soa
  Check the AA flag
  Repeat for the master and all the slaves
  Check the serial numbers match
dig @x.x.x.x example.com. axfr
  "Authority Transfer"
  Requests a full copy of the zone contents over TCP, as slaves do to master
  This will only work from IP addresses listed in the allow-transfer {...} section

## Slide 26: So now you have working authoritative nameservers!
But none of this will work until you have delegation from the domain above
That is, they put in NS records for your domain, pointing at your nameservers
You have also put NS records within the zone file
The two sets should match

## Slide 27: Any questions?
?

## Slide 28: TOP TEN ERRORS in authoritative nameservers
All operators of auth nameservers should read RFC 1912
  Common DNS Operational and Configuration Errors
And also RFC 2182
  Selection and Operation of Secondary DNS servers

## Slide 29: 1. Serial number errors
Forgot to increment serial number
Incremented serial number, then decremented it
Used serial number greater than 232
Impact:
  Slaves do not update
  Master and slaves have inconsistent data
  Caches will sometimes get the new data and sometimes old - intermittent problem

## Slide 30: 2. Comments in zone files starting '#' instead of ';'
Syntax error in zone file
Master is no longer authoritative for the zone
Slaves cannot check SOA
Slaves eventually expire the zone, and your domain stops working entirely
Use "named-checkzone"
Use "tail /var/log/messages"

## Slide 31: 3. Other syntax errors in zone files
e.g. omitting the preference value from MX records
Same impact

## Slide 32: 4. Missing the trailing dot
; zone example.com.
@ IN MX 10 mailhost.example.com
becomes
@ IN MX 10 mailhost.example.com.example.com.
; zone 2.0.192.in-addr.arpa.
1 IN PTR host.example.com
becomes
1 IN PTR host.example.com.2.0.192.in-addr.arpa.

## Slide 33: 5. NS or MX records pointing to IP addresses
They must point to hostnames, not IP addresses
Unfortunately, a few mail servers do accept IP addresses in MX records, so you may not see a problem with all remote sites

## Slide 34: 6. Slave cannot transfer zone from master
Access restricted by allow-transfer {...} and slave not listed
Or IP filters not configured correctly
Slave will be lame (non-authoritative)

## Slide 35: 7. Lame delegation
You cannot just list any nameserver in NS records for your domain
You must get agreement from the nameserver operator, and they must configure it as a slave for your zone
At best: slower DNS resolution and lack of resilience
At worst: intermittent failures to resolve your domain

## Slide 36: 8. No delegation at all
You can configure "example.com" on your nameservers but the outside world will not send requests to them until you have delegation
The problem is hidden if your nameserver is acting both as your cache and as authoritative nameserver
Your own clients can resolve www.example.com, but the rest of the world cannot

## Slide 37: 9. Out-of-date glue records
See later

## Slide 38: 10. Not managing TTL correctly during changes
e.g. if you have a 24 hour TTL, and you swing www.example.com to point to a new server, then there will be an extended period when some users hit one machine and some hit the other
Follow the procedure:
  Reduce TTL to 10 minutes
  Wait at least 24 hours
  Make the change
  Put the TTL back to 24 hours

## Slide 39: Practical
Create a new domain
Set up master and slave nameservice
Obtain delegation from the domain above
Test it